LatencyMeasure
A tool to measure latency
from keyboard or mouse input
to a visual response on the screen.

© 2020 by Christian.Lorenz@gromeck.de
This file is part of LatencyMeasure.
LatencyMeasure is free software: you can redistribute it and/or modify it under the terms of the GNU General Public License as published by the Free Software Foundation, either version 3 of the License, or (at your option) any later version.
LatencyMeasure is distributed in the hope that it will be useful, but WITHOUT ANY WARRANTY; without even the implied warranty of MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the GNU General Public License for more details.
You should have received a copy of the GNU General Public License along with LatencyMeasure. If not, see <https://www.gnu.org/licenses/>.

# Introduction
The LatencyMeasure device is used to measure the latency from a human input device (HID) to the response on the screen. This overall latency is sometimes called lag[1], input lag or finger-to-eye-latency.
[1] https://en.wikipedia.org/wiki/Lag
The measured overall latency is the sum of all signal processing, bus transfers, refresh rates, response times, etc.

The complete project is published on GitHub under
https://github.com/gromeck/LatencyMeasure
The distribution contains the circuit, a PCB layout, a device enclosure, sensor mount, the devices software as well as test clients for Linux.
# Device hardware
The device is based on an Arduino[2] compatible micro controller board. This board has to be capable to emulate keyboard and mouse via USB (32u4- oder SAMD-micro-based controllers).
[2] https://en.wikipedia.org/wiki/Arduino
Item	Specification
Controller Board	SparcFun Pro Micro
CPU	ATMEL[3] ATmega32U4
CPU frequency	8MHz
Measurement resolution	1ms
Number of digital inputs used	3
Number of digital outputs used	3
Number of analog inputs used	2
USB connector	yes, for keyboard and mouse HID emulation
Power	via USB connector
Sensor connector	via cinch connector
[3] https://en.wikipedia.org/wiki/Atmel

# Build the Software
If not already done, clone the repository
git clone git@github.com:gromeck/LatencyMeasure.git
## Software of the micro controller
### Arduino IDE support for the device
To install the Arduino IDE support for the used micro controller follow the instrutions found here:
https://github.com/sparkfun/Arduino_Boards
If this extension is installed correctly, the Arduino IDE should offer the board type „SparcFun Pro Micro 3.3V/8MHz“. Select it!
After connecting the micro controller to your host, it should appear as „/dev/ttyAMC<number>“ or „/dev/ttyUSB<number>“. Select it!
### Adding necessary libraries
Ensure that the following libraries are installed in the Arduino IDE environment:
Adafruit SSD1306
All other necessary software components are already contained in the Arduino IDE environment.
### The sketch
Start the Arduino IDE and open LatencyMeasure.ino sketch from the directory ./LatencyMeasure/LatencyMeasure/.
If the former steps were successfully done, the code can by compiled and linked. After finally uploading the sketch into the controller with the Arduino IDE, the controller should reset and startup with its splash screen and prompting in the main menu.
## Test clients
LatencyMeasure comes with a set of different test clients which can be used in different setups. All test clients run under Linux.
### Ncurses-based test client
This clients can be used in text console environments, or, of course, in the text console of a graphical shell like Xterm or others.
This implementation can be found in ./LatencyMeasure/TestClient/ncurses.
To configure the test client, do
./configure
If missing libraries or necessary tools are reported, fix them and rerun.
To build the executable, run
make
Finally, the client can be started with
./LatencyTest
The test client should appear like this:

### Qt-based test client
This client can be used in graphical environments like X11 or Wayland.
This implentation can be found in ./LatencyMeasure/TestClient/Qt4.
To build the test client, do
./build.sh
If missing libraries or necessary tools are reported, fix them and rerun.
Finally, the client can be started with
./LatencyTest
The test client should appear like this:

### Web-based test client
This client is implemented in a single HTML file and makes use of JavaScript.
This implentation can be found in ./LatencyMeasure/TestClient/HTML.
To run it, simply point a browser to ./index.html and follow the instructions.
The test client should appear like this:

# Use the device
The following section describes the use of the device from calibration to the measuring procedure.
## Connectors
The device has two connectors:
- USB
  The USB port is connected to the system under test. The device will emulate a keyboard respectively a mouse.
- Sensor
  This cinch connector is used to plug in the sensor.
## Buttons
The device has four buttons:
- RST is the reset button which simply restarts the device
  This is helpful when a series of measurements should be stopped.
- MENU is the button to switch between different choices which are shown in to bottom line of the display.
- OK is the button to select the selected option or menu item.
- SCREENSHOT is the button to dump the current display content of the USB link (see section 4.6).
  This button is not available from the outside of the enclosure.
## Calibration
A test client is used for the calibration procedure. The test clients always use a change from black to white on the screen whenever the key or mouse event occurs. To ensure a correct detection of black respectively white on the screen, the devices photo transistor has to be calibrated.
1. Connect the devices USB to power it up.
2. Select “Calibrate Sensor” from the menu and press OK.
3. Start one of the test clients.
4. Place the sensor over the sensor area of the test client.
5. Press OK once more on the device. The device will show the voltages of the photo transistor (Vin) and the reference voltage (Vref).
6. Write down Vin over black and white areas and compute the average between black and white values.
7. On the printed circuit you will find the trimmer R2.
8. Adjust the reference voltage Vref to the computed average.
Whenever the sensor area is switched from black to white or vice versa, the current detected value should be shown as DARK or BRIGHT on the devices display very spontaneously.
## Run the built-in test
The LatencyMeasure device has a built-in test procedure to verify the detection and check the devices response time. The response time should always be <2ms.
1. Connect the devices USB to power it up.
2. Select “Test Timing” from the menu and press OK.
3. Place the sensor over the test LED.
4. Select once more OK to start the verification.
5. The LED lights up with doubling the time between each times.
6. The device measures the time between the flashes.
7. After the test series is done, the overall result is shown.
A single failing measurement is still fine, repeat the procedure in that case.
## Configure measurement
### Series of Measure
The device is capable to run series of measurements without user action.
Select values of 1 (single), 10, 25 or 50 measurements.

### Measure Pause
The device will perform a pause between each measurement when doing series.
Select values of 500ms, 1s, 5s or 10s pause.

### HID Device Type
The device can act as a keyboard as well as a mouse.
Select values of Mouse or Keyboard.

### HID Mouse Button
If the device operates as a mouse, the emulated mouse button can be configured.
Select values of left, middle or right.

### HID Keyboard Key
If the device operates as a keyboard, the emulated key can be configured.
Select values of <SPACE>, <RETURN> or <F10>.

### Timer start at …
Whenever a key or mouse button event is emulated, the devices first transmits the key/button down event, and after a pause of 50ms the key/button up event.
Some environments react upon the first event (e.g. the text console), some do react on the second one (mostly graphical environments except the GUI requests the key/button down event).
This configuration controls whether timing starts upon the first or second one.

### Exit config
Select this entry to return to the main menu.

## Screnshots
As a special or hidden feature, the device can dump the current content of the OLED display via the serial connection as a PBM[4] bitmap (P1). This format is ASCII-based and uses one bit per pixel.
[4] https://de.wikipedia.org/wiki/Portable_Anymap
The screenshot is triggered by the hardware switch 3 on the PCB.
The software distribution contains the script
./LatencyMeasure/Ressources/Screenshots/getPBMviaSerial.sh
to receive a screenshot from the serial link, and directly convert it to a colorized PNG.
## Measure latency
Use one of the test clients to measure the latency in the requested environment.
Ensure that the device was calibrated.
1. Connect the devices USB to power it up.
2. Select “Measurement” from the menu and press OK.
3. Start the test client and setup the sensor to be over the sensor area on the screen.
4. Depending on the configuration, a single measurement or a series of measurements is performed.
5. When the measurement is done, the result is displayed on the device.
The displayed values are
ok	The number of successfully performed measurements.
total	The total number of performed measurements.
min	The smallest value of measured latency in milliseconds.
avg	The average value of measured latency in milliseconds.
max	The highest value of measured latency in milliseconds.

# Interpret measured latency values
## Latency from input to output
The following table shows the different steps in the overall chain between input and output.
Step	Explanation	Typical Latency
USB	The input is processed from the HID device via a USB hub into the USB host controller, passed over the system bus, queued and processed by the kernels IO-system.	<1ms
GUI	The GUI toolkit receives the input from the IO-System, does the event-to-widget correlation, and passes the input as an event to the application.	<1ms
Application	The input is processed by the application, special processing is performed, like DB or file operation, computations, or what ever this event should do. / The application also triggers the output.	<1ms for quick operations or asynchronous processing
GUI	GUI toolkit processes the instruction from the application to initiate a change on the GUI (e.g. drawing the changed widget).	<1ms
Network layer	This layer is missing in a local setup. In an environment where the display is forwarded via VNC, RDP, X11, or any other technologie, this might produce high latency, as multiple network messages are passed in the processing of events. / This layer not always at this point in the stack; this simply depends on the technology.	n * RTT[5]
Graphical sub-system	The graphical sub-system (like X11 or Wayland) processes the instruction on base of drawing primitives. These are processed (e.g. clipping, Z-axis, …) and the graphical operations are passed to the graphic card.	<1ms
Graphic card driver	This component does the translation from the graphical sub-system into operations that work on the graphic cards video memory.	<1ms
Graphic card	The video memory is transferred via the display connection (eg. VGA, HDMI, DisplayPort, …) to the displaying device.	<1ms
Monitor signal processing	The monitor processes the stream of incoming data and pushes this to the LED panel. This doesn’t produce a constant latency, as this is done in a certain frequency.	16.6ms @ 60Hz / 10ms @ 100Hz / 6.94 @ 144Hz
Monitor display	Finally the response time[6] of the monitor depends on the used technology. This is normally measured in grey-to-gray	>1ms for TN[7] panels / >4ms for IPS[8] panels
[5] https://en.wikipedia.org/wiki/Round-trip_delay
[6] https://en.wikipedia.org/wiki/Response_time_(technology)#Display_technologies
[7] https://en.wikipedia.org/wiki/Thin-film-transistor_liquid-crystal_display#Twisted_nematic_(TN)
[8] https://en.wikipedia.org/wiki/IPS_panel

## Typical Latency values
The following tables shows the typical overall latencies with the different test clients and environments (measured in a series of 10).
Test Client	Environment	min [ms]	avg [ms]	max [ms]
ncurses	X11/xterm	6	22	35
ncurses	FB/console	20	29	37
Qt4	X11	53	54	57
HTML/Firefox 78.x	X11	55	65	78
HTML/Chrome 83.x	X11	67	73	80

## Notes
Whenever you change the monitor, re-calibrate, as different monitors have different brightness.
In a local display setup you will measure latency values with an empirical variance at least of the refresh rate of the monitor.
If you have to compare values between different setups – especially when you want to measure network impact – try to use the same monitor. Also check the specification of the other used hardware components (eg. USB speed, network speed, display standard and its speed, monitor refresh rate and response times).